## Slide 1
WIRELESS
COMMUNICATION
Nikhil 112316031
Visweswar 112316009
Vinit 112316010
Sangamesh 112316041
Bhavya 112316012
Energy-Aware Online Positioning of UAV Base Stations in Dynamic Networks

## Slide 2
PROBLEM STATEMENT
When a terrestrial base station fails, communication is lost, and drone-mounted base stations are dynamically deployed to fill the coverage gap. However, current algorithms designed to position these drones focus solely on maximizing network capacity, causing the drone to constantly move to chase the best possible signal. This continuous movement is highly inefficient because it ignores the significant energy costs associated with flying. Therefore, a new approach is needed that balances network performance with movement costs, ensuring the drone only relocates when the communication improvement justifies the energy spent.

## Slide 3
BASIC TERMINOLOGY & BACKGROUND
  Coverage Hole: Area where users receive no or insufficient signal, typically caused by a site failure
  Aerial Base Station (Aerial-BS): A base station mounted on a UAV, offering a flexible and agile alternative to fixed terrestrial infrastructure.
  Cell Individual Offset (CIO): Bias in cell selection used to shift users between cells →Helps balance load
  Traffic Hotspots: Sudden surges in network demand caused by large crowds (festivals, sports events) or displaced populations during emergencies.

## Slide 4
BASIC TERMINOLOGY & BACKGROUND
  QoS (Quality of Service): A measure of the overall performance of the network, often quantified by throughput, signal strength, or call success.
  CSR (Call Success Rate): The fraction of initiated calls that successfully maintain a connection and meet minimum bit rate requirements. Main performance metric used in the paper
  Online Positioning: A real-time approach where the UAV moves and adapts its position dynamically based on live measurements rather than pre-planned coordinates.
  Air-to-Ground (A2G) Channel: The wireless link between the UAV and ground users, characterized by a higher probability of Line-of-Sight (LoS) compared to terrestrial links.

## Slide 5
OBJECTIVE OF THE RESEARCH PROBLEM
The Core Challenge: Positioning for Performance
The Deployment Trade-off: Determining the optimal 3D position (x, y, z) is difficult because it depends on unknown factors like user distribution and local propagation environments.
The Core Challenge: Positioning for Performance
Dynamic Adaptation: Since users move (User Mobility), the UAV must be able to track the "optimal" position in real-time without manual reconfiguration.
Capacity vs. Coverage: UAVs must decide whether to move toward a traffic hotspot to provide capacity relief or stay near a site failure to patch a coverage hole.

## Slide 6
OBJECTIVE OF THE RESEARCH PROBLEM
Data-Driven Online Algorithm: Develop a real-time algorithm to optimize the position of a drone-mounted base station during network disruptions.
Continuous Adaptation: Dynamically adjust to a changing environment, including variations in user distribution and moving traffic hotspots.
Real-Time Metrics: Utilize practically measurable network data (like cell load) instead of relying on prior environmental knowledge or pre-deployment training.
The Shift Toward Energy-Awareness
Performance Optimization: Achieve near-optimal Call Success Rate (CSR) to maximize the fraction of successful connections in dynamic scenarios.

## Slide 7
SIMULATION AND RESULTS

## Slide 8
  Network: 12 sites, 3 sectors each (36 cells), hexagonal layout with wraparound
  Environments: Urban (500 m ISD, capacity-limited) & Rural (3500 m ISD, coverage-limited)
  Antenna Model: Directional BS antennas; drone uses simplified antenna with lower transmit power
  Propagation:Separate models for BS–UE and Drone–UE links
  Includes LoS/NLoS conditions
  Uses environment parameters (α, β, γ)
  Shadow fading and minimum coupling loss considered
  Traffic: Random user arrivals with a traffic hotspot (higher load region)
  Static users, fixed minimum data rate
  Resource Management:
  User connects to best signal (with bias)
  Admission control + fair scheduling
  Handover and call drop conditions included
  Performance Metric: Call Success Rate (CSR)
MODELING ASSUMPTIONS

## Slide 9
SIMULATION PARAMETERES

## Slide 10
ALGORITHM

## Slide 11
  The drone’s altitude is fixed at 120 m and the Cell Individual Offset (CIO) is set to 0 dB, based on insights from the base paper indicating minimal impact on overall performance.
  Simulations were conducted for a duration of 90 minutes, averaged over 4 independent runs, compared to the 4-hour simulation window used in the base study.
  To compensate for the shorter simulation duration and to ensure system robustness, higher user arrival rates were considered in both urban and rural scenarios.
  Due to these modified simulation conditions, the obtained results show slight quantitative deviations from the base paper.
  However, the results continue to demonstrate consistent performance trends, validating the effectiveness of the proposed approach.
SIMULATION ASSUMPTIONS

## Slide 16
LIMITATIONS
The base paper does not account for energy-related constraints of the UAV, implicitly assuming unlimited battery capacity and neglecting the impact of movement on energy consumption. It focuses solely on optimizing network performance without considering the trade-off between performance gains and the energy cost of repositioning the drone. Continuous movement of the UAV is allowed without any penalty, which is unrealistic given that propulsion is one of the most energy-intensive operations in UAV systems. As a result, the proposed approach may lead to inefficient energy usage and reduced operational feasibility in real-world deployments.

## Slide 17
The proposed system uses a simplified discrete energy model to enable real-time decision-making. Energy consumption is calculated per time step, where the UAV consumes a fixed amount of energy α when it moves and a smaller amount β when it hovers. This model does not account for factors such as velocity, acceleration, altitude changes, or aerodynamic effects, and focuses only on propulsion energy while ignoring communication-related energy consumption. Although this is a simplified approximation, it significantly reduces computational complexity and allows the UAV to make fast energy-aware positioning decisions in dynamic environments.
ENERGY MODEL

## Slide 19
  Significant Reduction in Movement
    Approximately 425 fewer movement steps on average
    Consistent improvement observed across all 44 scenarios
  Impact on Network Performance (CSR)
    Majority of scenarios exhibit negligible change in CSR
    25 scenarios show improvement in CSR
    Worst-case degradation remains limited (≈ −0.02)
  Performance–Energy Trade-off
    Substantial reduction in movement achieved with minimal performance loss
    In several cases, reduced movement leads to improved stability and better CSR
  Scenario-Specific Behavior
    Urban (DU): Higher variability; slight performance drop in high-saving cases
    Rural (RU): More stable performance; CSR changes remain close to zero
Key Observations & Insights

## Slide 20
The energy-aware positioning algorithm delivers significant efficiency gains by reducing unnecessary UAV movement while maintaining near-equivalent network performance. In several scenarios, it even achieves improved performance, demonstrating the practical benefits of incorporating energy awareness into real-time positioning decisions. Despite its simplified design, the approach produces meaningful and reliable results, making it suitable for real-world deployment. Furthermore, there is considerable scope for future work, including the integration of more realistic UAV energy and mechanical models, as well as extending the framework to support coordinated multi-UAV networks for enhanced scalability and performance.
CONCLUSION

## Slide 21
References
T. R. Pijnappel, J. L. van den Berg, S. C. Borst and R. Litjens, "Online Positioning of a Drone-Mounted Base Station in Emergency Scenarios," in IEEE Transactions on Vehicular Technology, vol. 73, no. 4, pp. 5572-5586, April 2024, doi: 10.1109/TVT.2023.3329960
Energy-aware Relay Positioning in Flying Networks
A survey on UAV assisted wireless communications: Recent advances and future trends

## Slide 22
THANK YOU